[Doc] [EE] [Enter] ... [On]

You can even try to access the maintenance menu without removing the batteries (think CX) by 
holding down
doc, EE, and enter 
while I pressed the reset button on the back.

What troubleshooting can I try if the TI graphing calculator will not turn on?

Last Updated: 08-DEC-2009 20:42:44

Note: Information on battery precautions and replacement can be found in the case entitled "Instructions for Replacing Batteries In a TI Graphing Calculator".

For the TI-Nspire™ Family:

1. Remove the keypad (for TI-Nspire) or the battery door (for TI-Nspire CAS) and remove at least 1 battery from each column of batteries. After 2-5 seconds, reinsert the batteries and turn the unit on. This will cause the unit to reboot the operating system.

2. Remove the keypad (for TI-Nspire) or the battery door (for TI-Nspire CAS) and remove at least 1 battery from each column of batteries. After 2-5 seconds, reinsert the batteries and LEAVE THE UNIT OFF (do not turn on and then back off). Hold down [Home] [Enter] [P], and while holding these keys, press [On]. The device will boot up as in the previous reset, but will display a menu with the following options. Please try options 1, 2, 3, and 4 in that order. ** The [Home] key is located at the top right of the TI-Nspire keypad and has a picture of a house on it.

Note: • TI-Nspire family model options 2 and 4 above require that the OS be reinstalled. The reset menu will only display if the unit is off and batteries have been removed/replaced as described above.

• For the TI-Nspire handheld, you need to use the TI-Nspire keypad and not the TI-84 Plus keypad to be able to attempt these resets.

1. Cancel - The most non-intrusive reset option; no changes are made, the unit restarts.

2. Delete Operating System – The operating system will be deleted without deleting any documents.

3. Delete Document Folder Contents – This will delete the user’s documents, but will not delete the OS.

4. Complete Format – This will delete the OS and all documents for a total erase of memory.

For the TI-83 Plus Family, TI-84 Plus Family:

Caution:  The resets described in these troubleshooting steps will cause a loss of applications, programs and data. If at all possible please create a backup using TI Connect™ first.

1. Try a new set of AAA batteries.

2. Adjust the contrast by pressing and releasing the [2nd] key followed by pressing and releasing the up arrow; repeat as necessary. To adjust or lighten the display, use the down arrow.

3. Remove one of the AAA batteries. Press and hold the [CLEAR] key. While holding [CLEAR], reinsert the AAA battery and then turn the calculator on. The calculator should display the message "RAM Cleared". Release the [CLEAR] key and then press it one more time to remove the message.

4. Remove one of the AAA batteries. Press and hold the [DEL] key. While holding [DEL], reinsert the AAA battery and then turn the calculator on. The calculator should display "Waiting...Please install calculator software now". Follow the instructions for the TI-83 family or TI-84 Plus family to reinstall the calculator operating system.

5. Remove all of the batteries including the round lithium battery for 5 minutes. After the 5 minute period, reinsert all of the batteries and turn the calculator on. Adjust the contrast if necessary.

For the TI-89 Family, TI-92 Family, and Voyage™ 200:

1. Try a new set of AAA batteries (AA batteries on the TI-92 Family).

2. Adjust the contrast by pressing and releasing the Diamond key followed by pressing and releasing the [+] key; repeat as necessary. To adjust or lighten the display, use the [-] key.

3. Users of the TI-89 Titanium or Voyage 200 should see the following case before performing the following reset procedure to prevent the loss of valuable Apps.

On the TI-92 family or Voyage 200, hold the [2nd] key and the [hand] key, then press and release the [ON] key. On the TI-89 family, press and hold the [2nd] key, left arrow, and right arrow; then press and release the [ON] key. This should reinitialize the operating system, in which you should see a progress bar filling on the screen.

4. Remove one of the AAA or AA batteries. Press and hold the [APPS] key, and while holding the [APPS] key, replace the battery and turn the unit on. TI-89, 92 Plus, or Voyage 200 users should see "Press I to install code...", and should press the [9] key. The calculator should then say, "Waiting to receive...". TI-89 Titanium users should see "Waiting to receive..." or "Waiting to received OS...". You will need to restore the calculator's operating system.

For the TI-73 Family, TI-80, TI-81, TI-82, TI-83, TI-85, and TI-86:

1. Try a new set of AAA batteries.

2. Adjust the contrast by pressing and releasing the [2nd] key followed by pressing and releasing the up arrow; repeat as necessary. To adjust or lighten the display, use the down arrow.

3. Remove one of the AAA batteries. Press and hold the [ON] key for 20 seconds. Reinsert the AAA battery and then turn the calculator on.

4. Remove all of the batteries including the round lithium battery for 5 minutes. After the 5 minute period, reinsert all of the batteries and turn the calculator on. Adjust the contrast if necessary.

Access the link following for detailed information regarding warranty coverage.

If the suggestions do not alleviate the problem, please contact TI-Cares for information regarding service.